## Slide 1
UNIVERSITY OF SWABI · DEPARTMENT OF COMPUTER SCIENCE
Water Angel
Smart IoT-Based Water Management & Monitoring System
Presented by Salman Khan (Roll No. 111, BS CS – Batch 12, Section C) Semester : 4th
Team Members Shayan Asim (93) · Muhammad Hamza Jamal (57) Semester : 4th
Supervisor Dr. Saeed Ahmad — Assistant Professor, Dept. of Computer Science
Semester Project(IoT) Presentation · Departmental Review

## Slide 2
WHY THIS PROJECT
Traditional Water Tanks Run on Guesswork
Manual pump operation leads to waste, equipment damage, and zero visibility into water level or quality.
Overflow & Underflow
Delayed manual switching wastes clean water or causes shortages
Wasted Electricity
Continuous or mistimed pump runtime drives up energy bills
Pump Damage
Dry-running conditions go undetected and wear out equipment
No Visibility
No real-time data on current water level at all
No Remote Access
Users can't check or control the pump while away
Unknown Water Quality
TDS / contamination levels are never measured
Lack of Automation
Every action depends on someone remembering to switch the pump
No Smart Control
No intelligent decision-making exists in conventional setups
Water Angel — Project Presentation
2

## Slide 3
OUR APPROACH
Water Angel: An Offline-First Smart Solution
An ESP32-based system that automates pump control using real-time water level and quality sensing — synced to the cloud and accessible from anywhere, while continuing to operate fully even when the internet goes down.
ESP32 Microcontroller
Sensor reading, pump logic, Wi-Fi & local control
Supabase Cloud Backend
Real-time sync, authentication & secure storage
Progressive Web App
Remote monitoring, control & configuration
Water Angel — Project Presentation
3

## Slide 4
GOALS
Project Objectives
1
Automate pump control via real-time water-level sensing
2
Prevent overflow and underflow conditions entirely
3
Monitor water quality continuously using a TDS sensor
4
Enable remote monitoring & control through a mobile app
5
Allow custom tank-height and threshold configuration
6
Support manual override alongside automatic mode
7
Guarantee offline-first, uninterrupted operation
8
Generate real-time analytics and intelligent alerts
Water Angel — Project Presentation
4

## Slide 5
HOW IT FITS TOGETHER
System Architecture
HARDWARE LAYER
Sensing — ultrasonic level + TDS quality readings
Control — relay-driven automatic pump switching
Local feedback — LCD, LED indicators & buzzer
Persistence — config stored safely in EEPROM
SOFTWARE LAYER
PWA — remote monitoring, control & configuration
Supabase — storage, auth & real-time sync
Analytics — usage trends & intelligent alerts
Offline engine — full local function w/o internet
Water Angel — Project Presentation
5

## Slide 6
INSIDE THE BUILD
Core Hardware Components
ESP32 Microcontroller
Brain of the system — sensing, control & connectivity
Ultrasonic Sensor
Measures distance to water surface for level %
TDS Sensor
Detects dissolved solids to flag poor water quality
Relay Module
Electronic switch driving the water pump safely
Water Pump
Fills the tank — runs in auto or manual mode
16×2 I2C LCD
Local display for level, TDS, pump status & mode
LEDs & Buzzer
Visual / audible alerts for critical conditions
EEPROM Storage
Retains Wi-Fi, thresholds & calibration on reboot
Setup Button
Hold 3s to open Wi-Fi provisioning hotspot
Water Angel — Project Presentation
6

## Slide 7
WIRING IT UP
Circuit Design
ESP32 connected to the ultrasonic level sensor, TDS sensor, relay module, LCD, LEDs and buzzer on a breadboard prototype
Water Angel — Project Presentation
7

## Slide 8
BUILT & TESTED
From Diagram to Working Prototype
Water Source
Water Tank
Main Circuit Board
Water Angel — Project Presentation
8

## Slide 9
BEHIND THE APP
Software Architecture
Water Angel PWA
The primary interface — monitor levels, control the pump, configure thresholds, view analytics, and receive alerts from any browser.
Supabase Backend
Cloud database, authentication and real-time sync. Sensor readings, pump status, and configuration all live here.
Offline-First Engine
Critical functions — level sensing, TDS monitoring, automatic pump control — keep running with zero internet.
When connectivity returns, the ESP32 automatically resumes syncing readings, status, and settings with the cloud.
Water Angel — Project Presentation
9

## Slide 10
FIRMWARE ENGINEERING
Dual-Core FreeRTOS Architecture
HTTP calls to Supabase were blocking the sensor loop — causing overflow. Splitting across two cores eliminated the problem entirely.
CORE 1 — SENSOR & CONTROL
Ultrasonic water-level reading
TDS water quality sampling
Pump ON / OFF control logic
LCD, LED & buzzer feedback
Setup button & beep handler
Priority 2 · Cycle every 50 ms · Pump reacts in < 550 ms
CORE 0 — CLOUD & NETWORK
Supabase GET / POST (blocks up to 10 s)
fetchDeviceInfo & fetchPumpSettings
sendSensorData every 30 s
WiFi connection & auto-retry
Re-syncs settings on reconnect
Priority 1 · Yield every 100 ms · Never touches sensor pins
SensorSnapshot
level · tds · pumpOn
pumpMode · runtimeMin
CloudSettings
thresholds · tankHeight
pumpMode · manualCmd
FreeRTOS
Queues
Result: HTTP calls can now block Core 0 for up to 10 seconds — pump control on Core 1 is completely unaffected. Overflow eliminated.
Water Angel — Project Presentation
10

## Slide 11
WATER ANGEL PWA · TAB 1
Home Dashboard
A single real-time overview of the entire water management system.
Live ESP32 connectivity status
Always know if the device is online and when it last reported in
Visual tank-level gauge
Animated fill graphic shows the exact water percentage at a glance
Water quality at a glance
TDS reading with a clear Safe / Unsafe indicator
Pump status & last update
Current ON/OFF state plus the most recent sync timestamp
24h history & smart insights
Usage trend graph with auto-generated tips like refill timing
Water Angel — Project Presentation
11

## Slide 12
WATER ANGEL PWA · TAB 2
Analytics Dashboard
Turns raw sensor readings into usage trends, scores, and recommendations.
7-day water level history
Trend line shows refill events and gradual consumption
Consumption & TDS trend analysis
Daily usage bars and a 7-day water-quality trend line
Pump activity tracking
Logs how often and how long the pump has been running
Water Efficiency Score
A single number summarizing how well the tank is managed
Weekly smart report
Auto-generated recommendations, e.g. peak usage windows
Water Angel — Project Presentation
12

## Slide 13
WATER ANGEL PWA · TABS 3 & 4
Control & Alerts
PUMP CONTROL
Switch between Automatic and Manual pump modes
Set custom tank height for accurate level %
Adjust Upper / Lower / Critical thresholds live
ALERTS
Sudden-drop / leak detection
High-TDS water quality warnings
Critical low-level refill alerts
Every alert is timestamped & categorized
Water Angel — Project Presentation
13

## Slide 14
WATER ANGEL PWA · TAB 5
Profile & Account
Account management, device pairing, and system configuration in one place.
Device pairing
Connect the app to a specific Water Angel unit via its unique Device Key
Notification preferences
Independently toggle Low Water, High TDS, Pump Status & Anomaly alerts
Wi-Fi & calibration
Update Wi-Fi credentials and recalibrate tank height anytime
Account security
Change password and sign out safely from the connected device
Water Angel — Project Presentation
14

## Slide 15
END TO END
Water Angel — Project Presentation
15

## Slide 16
PROVEN, NOT JUST PLANNED
Results & Achievements
Every core feature was implemented, tested, and verified working end-to-end.
Automatic pump control working reliably
Offline-first operation verified under no internet
Cloud synchronization tested successfully
Real-time monitoring fully implemented
Water quality (TDS) monitoring implemented
Alert & notification system live
Intelligent analytics dashboard developed
Wi-Fi provisioning & remote configuration working
Water Angel — Project Presentation
16

## Slide 17
REAL-WORLD IMPACT
Benefits & Deployment Areas
KEY BENEFITS
Reduces water wastage from overflow
Saves electricity via optimized pump runtime
Prevents pump damage from dry-running
Real-time visibility into level & quality
Remote accessibility from anywhere
DEPLOYMENT AREAS
Residential homes & domestic tanks
Apartment buildings & housing societies
Educational institutions & hostels
Commercial buildings & small industries
Agricultural farms & irrigation systems
Water Angel — Project Presentation
17

## Slide 18
WHAT'S NEXT
Future Enhancements
Water Angel v1.0 is complete — here's where it can grow next.
AI-Based Prediction
Forecast consumption patterns and pre-emptively schedule refills
Leakage Detection
Identify abnormal flow or sudden drops and alert before water is lost
Solar-Powered Operation
Remove dependency on grid power for full energy independence
Mobile Push Notifications
Native push alerts instead of in-app notifications only
Advanced Water Quality
Add sensors for pH, turbidity & chlorine beyond TDS alone
Smart Community Management
Scale a single dashboard across multiple connected tanks
Water Angel — Project Presentation
18

## Slide 19
Water Angel modernizes traditional water management — reducing waste, saving energy, and enabling smart, remote, real-time control.
Thank You
Questions & Answers
Salman Khan
BS Computer Science · University of Swabi
Scan for Water Angel App